## Slide 1
Geometric Analysis Based Algorithms for Effective Representation and Detection of Curves with Application to Tracking Moving Dim Target
Advisor: Dr. Ofer Levi
By: Galit Volpert

## Slide 2
Presentation Outline
Motivation
Objectives
Background
SHAS vs other X-ray approaches
Dynamic SHAS
Dim Target tracking application
Experiments methodology
Results

## Slide 3
Multiscale Geometric Analysis
Motivation
Detect, organize, represent, and manipulate
data
which nominally span a high-dimensional space
but
which contain important features
which are approximately concentrated on lower-dimensional subsets (curves, sheets, etc.).
http://www.ipam.ucla.edu/programs/long-programs/multiscale-geometry-and-analysis-in-high-dimensions/
Notes: Works done in the scientific area that deals with…..

## Slide 4
Motivation
n3 – voxels (cube), f(x,y,z)
-point field
Contains filaments and noise
Data of Interest
Notes: אלמנטים חוטים

## Slide 5
Motivation
Medical and Biological Imaging
Astronomy
Dim Moving Objects Tracking
Applications
https://www.pinterest.com/pin/490540584389823063/
https://www.jvejournals.com/article/20724
D. L. Donoho a, O. Levi a, J.-L. Starck b and V.J.Mart´ınez c ,Multiscale Geometric Analysis for 3-D Catalogues
Mehul P. Sampat, Alan C., Bovik B., Mia K. Markey, Classification of mammographic lesions into BI-RADS shape categories using the Beamlet Transform

## Slide 6
Motivation
Man-made dim moving target.
A point target.
Low SNR (barely seen by naked eye).
Dim Moving Objects Tracking
Multiscale
Dynamic - Mono-scale
?
Notes: Our interest is in the detection of a sub-pixel target, which is significantly smaller than pixel size, where there is no need to take into account the target point spread function, which is assumed to have its entire support inside a single pixel.
Multiscale based algorithm – develop by Boris Efrati in its thesis
Dynamic Mono-scale based algorithm – this thesis

## Slide 7
Objective
Validate the accuracy and efficiency of the Geometric approach X-ray transform algorithm named SHAS by comparing to other discrete X-Ray transform algorithm \
Analyze and present the Dynamic SHAS as a computationally efficient algorithm for dynamically computing X-Ray coefficients inside a sliding window.
Develop a Dynamic SHAS based tool for tracking a dim target.

## Slide 8
Background
X-Ray Transform
An integral transform mapping spatial data into the parametric space of line integrals
2D 3D
,L – 3D line , p point on L
Notes: "point and unit vector" 𝑅^6→𝑅^4

## Slide 9
Piecewise constant interpolation – interpolation of order zero
“smooth” interpolation – interpolation of higher orders
Interpolation Scheme
Background
Discrete X-ray transform
0
9
1
9
10
5
3
10
6
8
10
3
9
3
8
4
the length of the intersection between the line L
and the pixel [i,j]
Notes: The X-Ray transform is not uniquely defined in the discrete case because integration over a discrete array is not well defined, and requires a choice of interpolation of the discrete data into the continuous domain so the integral can be evaluated.
The Piecewise constant interpolation - widely used in image processing, as it is simple and consistent with the image display on the computer display
In the discrete case, the integral is replaced by a summation operator, and the line integral is defined as a weighted sum.

## Slide 10
X-driven
Y-driven
Fixed intercept, varying slope
Fixed slope, varying intercept
Slope-Intercept System
Background
Discrete Parameterization of Line Segments
X-driven
Z-driven
X-driven
Y-driven
Y-driven
Notes: Another aspect is choosing expressive set and parameterization of line segments for line integration
This system of lines corresponds to a family of lines that are equally sampled with respect to their slopes and not with respect to their angles, and the uniform spacing of lines in each projection varies with respect to the slope. This is not the natural choice and might be problematic for reconstruction applications like CT, but for the application of curve detection , it is sufficient.

## Slide 11
Background
Computation of X-ray
Computational Complexity – O(N) per coefficient
1
0
3
3
3
4
6
5
9
8
9
10
10
10
8
9
Fast Slant Stack (2003), Averbuch et. al.
Direct evaluation methods Fourier domain based methods
Equivalent to computing integrals over trigonometric interpolation of the sampled image. Tied to slope-intercept system.
Computational Complexity – O(log(N)) per coefficient
Notes: The FSS Algorithm developed by Averbuch et al. [3] computes a discrete 2D Radon Transform. The algorithm is based on the relation between the Radon (X-Ray) transform and the Fourier space, defined by the Projection-Slice Theorem, also known as the Central-Slice Theorem.

## Slide 12
Computation of X-ray
Fourier domain based methods
Background
Pseudo -Polar
Polar
https://www.semanticscholar.org/paper/1-Introduction-1-.-1-Polar-Fourier-Transform-Averbuch-Coifman/7666cfa5840217c65536bf6053268b72b50660c3
Notes: The projection slice theorem can be used for indirect computation of the radon transform by applying first a polar or polar like Fourier transform following a series of 1D FFT. The main drawback of this approach is that there is no fast and exact polar FFT, and therefore, one needs to compromise either on the computational complexity or the accuracy when computing polar Fourier transform. In order to overcome that, the FSS algorithm uses a fast and exact polar like Fourier Transform called the Pseudo-Polar FFT. The computational complexity of the pseudo polar FFT, (as well as for the entire FSS algorithm), is . The pseudo polar FFT computes the discrete set of Fourier coefficient over the pseudo polar gride
The pseudo polar grid differs from the polar grid by having concentric squares instead of concentric circles. Another difference is that the pseudo polar grid uses equally spaced slopes instead of equally spaced angles. The FSS transform is performed by applying a series of inverse 1D FFT's along the radial lines of the Pseudo-Polar grid. The resulting discrete set of radon coefficients is identical to the slope-intercept system with respect to the grid in the Radon space
The FSS algorithm can be generalized to 3D in several ways. For comparison and analysis, we used a computational approach that utilizes the operation of 3D shiring . Obviously, it is much easier to compute projection, which is a perfect parallel to one of the axis because than it is no more than a summation of rows or columns. So an effective approach for computing projections is first rotating the image in a way the desired projection becomes parallel to one of the axis. The 3D shiring is similar to 3D rotation and computationally efficient
The projection slice theorem can be used for indirect computation of the radon transform by applying first a polar or polar like Fourier transform following a series of 1D FFT. The main drawback of this approach is that there is no fast and exact polar FFT, and therefore, one needs to compromise either on the computational complexity or the accuracy when computing polar Fourier transform. In order to overcome that, the FSS algorithm uses a fast and exact polar like Fourier Transform called the Pseudo-Polar FFT. The computational complexity of the pseudo polar FFT, (as well as for the entire FSS algorithm), is 𝑂(𝑛^2 𝑙𝑜𝑔(𝑛)). The pseudo polar FFT computes the discrete set of Fourier coefficient over the pseudo polar gride
The pseudo polar grid differs from the polar grid by having concentric squares instead of concentric circles. Another difference is that the pseudo polar grid uses equally spaced slopes instead of equally spaced angles. The FSS transform is performed by applying a series of inverse 1D FFT's along the radial lines of the Pseudo-Polar grid. The resulting discrete set of radon coefficients is identical to the slope-intercept system with respect to the grid in the Radon space
The FSS algorithm can be generalized to 3D in several ways. For comparison and analysis, we used a computational approach that utilizes the operation of 3D shiring . Obviously, it is much easier to compute projection, which is a perfect parallel to one of the axis because than it is no more than a summation of rows or columns. So an effective approach for computing projections is first rotating the image in a way the desired projection becomes parallel to one of the axis. The 3D shiring is similar to 3D rotation and computationally efficient

## Slide 13
Background
SHAS Algorithm
Observation
Simultaneous calculation with serial memory access
Notes: I’ll start by demonstrating the main ideas in 2D …
The distribution of weights for line integral is similar for parallel line segments up to appropriate shifts

## Slide 14
Background
SHAS Algorithm
Merging Series of Grid Intersections 2D
-8 -7 -6 -5 -4 -3 -2 -1 0 1 2 3 4 5 6 7 8
-4 -3 -2 -1 0 1 2 3 4
(-2,1)
(-2,2)
(-3,2)
(-3,3)
(-4,3)

## Slide 15
Background
SHAS Algorithm
– The input, a 2D data array.
- The output, an array of the resulting coefficients of the X-Ray transform over the appropriate set of lines :
  - The index for the line-family (X or Y-driven).
  s - The slope index.
  t - The intercept index.
- The line fragments array for the line with slope s.
- The operator of the extension E, padding an array n wide and n tall to be n wide and 2n tall by adding extra rows of zeros symmetrically above and below the input argument.
- The trimmed shift operator (non-circular) over vectors of size 2n. Given any vector, the result of for any integer d is a vector, where an i-th element in v is identical to the element at the position i+d in w or zero if the index i+d exceeds matrix dimensions.

## Slide 16
SHAS Algorithm
Background
Merging Series of Grid Intersections 3D
Notes: The same idea in 3D

## Slide 17
Computation of X-ray
Background
Notes: merging three equispaced sequences defined by parameterizing the line L using a parameter such that L(t) = {x(t),y(t),z(t)} with L(0)= and L(1)=(the cube voxels corners, which are the end points of the line segment L). Defining the line segment L intersect a YZ-plane whenever t is a multiple of , an XZ--plane whenever t is a multiple of , and a XY-plane whenever t is a multiple of
merging three equispaced sequences defined by parameterizing the line L using a parameter 0≤ 𝑡 ≤ 1 such that L(t) = {x(t),y(t),z(t)} with L(0)= 𝑣_0 and L(1)= 𝑣_1 (𝑣_0,𝑣_1 the cube voxels corners, which are the end points of the line segment L). Defining ∆_𝑥=𝑥_1−𝑥_0 ,∆_𝑦=𝑦_1−𝑦_0 ,∆_𝑧=𝑧_1−𝑧_0 the line segment L intersect a YZ-plane whenever t is a multiple of 1∕|∆_𝑥 | , an XZ--plane whenever t is a multiple of 1∕|∆_𝑦 | , and a XY-plane whenever t is a multiple of 1∕|∆_𝑧 |

## Slide 18
Background
SHAS Algorithm
- The Input, a 3D voxel array.
The output, a 5D array of the resulting coefficients of the X-Ray, transforms over the appropriate set of lines:
  – The index for line-family (X, Y or Z-driven)
  - The pair of line slopes and the pair of line intercepts.
- The Line fragments array for Z-driven lines with slopes .
- The padded matrices of size n, by extra rows or columns of zeros, respectively.
- The trimmed shift operator (non-circular) over a matrix of size . Given any matrix, the result of for any integer d is a matrix, where an i-th row in A is identical to the row at the position i+d in B or zero if the index i+d exceeds matrix dimensions.

## Slide 19
SHAS vs other X-ray approaches
 | Direct Evaluation | Two-Scale Recursive approximations | Fast Slant Stack | SHAS
Accuracy |  |  |  | 
Time Complexity (Per Coefficient) |  |  | with a high constant factor | with a low constant factor
Memory Complexity |  |  |  | 
Memory Access | Not serial | Not serial | Serial | Serial
Line Set Flexibility | High | High | Very Low | Low
 | Direct Evaluation | Two-Scale Recursive approximations | Fast Slant Stack | SHAS
Accuracy |  |  |  | 
Time Complexity (Per Coefficient) |  |  |  | 
Memory Complexity |  |  |  | 
Memory Access | Not serial | Not serial | Serial | Serial
Line Set Flexibility | High | High | Very Low | Low
1 - Exact for Piecewise constant representation of the image.
2 - Exact for representing the image as smoothed trigonometric Interpolation of a sample pixel value.
3 - Relatively Coarse interpolation.
4 - 2D image / 3D image.
t (sec)
t (sec)
Image side size
Image side size
2D
3D
Notes: When applying The FSS transformation on an image with a single line, the FSS coefficients are more scattered than for the SHAS ones as there are based on Dirichlet kernel . The difference gets smaller and smaller when n increases. The SHAS is more robust as it includes only simple arithmetic operations like summation and multiplication vs. the FSS, which uses Fourier based interpolation.
Theoretically, the time complexity of the transforms operation per coefficient is O(n) for the SHAS algorithm and for the FSS algorithm for a image. However, although the FSS is asymptotically faster, its constant multiplier can be quite significant as it involves the application of the fractional Fourier Transform, which is more expensive than a standard FFT and uses complex arithmetic's. On the other hand, the constant multiplier of the SHAS algorithm is about two and involves summation and multiplication of real numbers. This explains the comparison results seen in the next figures where the SHAS is faster for small-medium image sizes.
The SHAS algorithm allows some flexibility regarding the choice of line set; Unlike the FSS, there are no constraints on the slopes, and any slope density and angular spacing are allowed. The only constraint is on the set of lines, which is limited to subsets of parallel equispaced lines with vertical or horizontal shifts in the 'basically' vertical or horizontal sets. On the other hand, the FSS algorithm is restricted to the pseudo-polar grid, which forces the system of lines to be equispaced with respect to the sloped.
When applying The FSS transformation on an image with a single line, the FSS coefficients are more scattered than for the SHAS ones as there are based on Dirichlet kernel . The difference gets smaller and smaller when n increases. The SHAS is more robust as it includes only simple arithmetic operations like summation and multiplication vs. the FSS, which uses Fourier based interpolation.
Theoretically, the time complexity of the transforms operation per coefficient is O(n) for the SHAS algorithm and 𝑂(𝑙𝑜𝑔 𝑛) for the FSS algorithm for a 𝑛×𝑛 image. However, although the FSS is asymptotically faster, its constant multiplier can be quite significant as it involves the application of the fractional Fourier Transform, which is more expensive than a standard FFT and uses complex arithmetic's. On the other hand, the constant multiplier of the SHAS algorithm is about two and involves summation and multiplication of real numbers. This explains the comparison results seen in the next figures where the SHAS is faster for small-medium image sizes.
The SHAS algorithm allows some flexibility regarding the choice of line set; Unlike the FSS, there are no constraints on the slopes, and any slope density and angular spacing are allowed. The only constraint is on the set of lines, which is limited to subsets of parallel equispaced lines with vertical or horizontal shifts in the 'basically' vertical or horizontal sets. On the other hand, the FSS algorithm is restricted to the pseudo-polar grid, which forces the system of lines to be equispaced with respect to the sloped.

## Slide 20
Two Scale Recursion
SHAS vs other X-ray approaches
Notes: Generally, an approximation of each line segment at the coarse-scale can be made by a connected chain of lines segment in the next finer scale.
the coarse-scale can be computed by summing the appropriate X-Ray coefficients from the next finer scale. Despite its elegant low theoretical complexity and compatibility with the multiscale beamlet structure, the results are not exact (except the case where the coarse-scale line has the same slope as its finer scale parts), and to increase the level of accuracy, one must apply oversampling or accurate and expensive interpolation. The second drawback of this approach is that despite the theoretical time complexity per coefficient in practice, the running time is much slower because of the required non-sequential access to the coefficients space, which is much bigger than the image space, especially in higher dimensions
Generally, an approximation of each line segment at the coarse-scale can be made by a connected chain of lines segment in the next finer scale.
the coarse-scale can be computed by summing the appropriate X-Ray coefficients from the next finer scale. Despite its elegant low theoretical complexity and compatibility with the multiscale beamlet structure, the results are not exact (except the case where the coarse-scale line has the same slope as its finer scale parts), and to increase the level of accuracy, one must apply oversampling or accurate and expensive interpolation. The second drawback of this approach is that despite the theoretical 𝑂(log⁡〖𝑛)〗 time complexity per coefficient in practice, the running time is much slower because of the required non-sequential access to the coefficients space, which is much bigger than the image space, especially in higher dimensions

## Slide 21
2D
Dynamic SHAS
As
X-driven
Y-driven
Notes: We first present the strategy for the 'Step Right' case. We denote by a zero-intercept offset as the smallest distance between the interception point of an X-driven line segment with slope s and the origin, is defined similarly for the Y-driven line segment.
For the X-driven lines, we need to recalculate the zero-intercept offset for each slope to update the line fragments array. Because the magnitude of the slopes is smaller or equal to one, we can ensure that its absolute zero-intercept offset value will never be higher than 0.5 by performing a shift of one if needed. Then we update the coefficients according to , and the corresponding updated fragment-array columns, where each coefficient is updated for the first or last or both columns instead of for all columns as in SHAS, and with two or fewer operations per column
Updating the coefficients of the Y-driven line is based on a consequent walk through adjacent pixels in , and adding or subtracting its weights to an appropriate coefficient with the current slope. Some coefficients may require up to n operations, and they are compensated for by a large set of coefficients that require only re-indexing.
The procedure for 'Step Left' is the same as 'Step Right' after reversing the order of slopes and column vectors , . The procedures for 'Step Up' and 'Step Down' are almost like 'Step Right' and 'Step Left,' where the X-driven lines are updated with Y-driven procedures and vice versa.
We first present the strategy for the 'Step Right' case. We denote by ∆_𝑥^0 (𝑠) a zero-intercept offset as the smallest distance between the interception point of an X-driven line segment with slope s and the origin, ∆_𝑦^0 (𝑠) is defined similarly for the Y-driven line segment.
For the X-driven lines, we need to recalculate the zero-intercept offset for each slope to update the line fragments array. Because the magnitude of the slopes is smaller or equal to one, we can ensure that its absolute zero-intercept offset value will never be higher than 0.5 by performing a shift of one if needed. Then we update the coefficients according to 𝑣^𝑖𝑛 , 𝑣^𝑜𝑢𝑡 and the corresponding updated fragment-array columns, where each coefficient is updated for the first or last or both columns instead of for all columns as in SHAS, and with two or fewer operations per column
Updating the coefficients of the Y-driven line is based on a consequent walk through adjacent pixels in 𝑣^𝑖𝑛 , 𝑣^𝑜𝑢𝑡and adding or subtracting its weights to an appropriate coefficient with the current slope. Some coefficients may require up to n operations, and they are compensated for by a large set of coefficients that require only re-indexing.
The procedure for 'Step Left' is the same as 'Step Right' after reversing the order of slopes and column vectors 𝑣^𝑖𝑛, 𝑣^𝑜𝑢𝑡. The procedures for 'Step Up' and 'Step Down' are almost like 'Step Right' and 'Step Left,' where the X-driven lines are updated with Y-driven procedures and vice versa.

## Slide 22
3D Dynamic SHAS
Dynamic SHAS
Notes: The Dynamic SHAS average update times for a step in each direction (X, Y, Z) for any specific driven lines were registered using C implementation with double precision running on Intel® Core™ i7-6700K CPU @ 4.00GHz
The reduced complexity:
The coefficients update takes roughly half of the SHAS update time.
The coefficients update in the X-direction takes around a third of the Y, Z direction update time.
The Z-direction update takes a little longer as C implementation use Row-major order, and our Z-direction update implementation takes column-major order, which is less cache-aware.

## Slide 23
3D– X-Driven update
Dynamic SHAS
Notes: The Strategy for the 3D case is based on the same principles for the 2D scenario with the following adjustments; The sliding window can move 'Step Forward' (Plus) and 'Step Backward' (Minus) in three different directions according to the axes X, Y, and Z. Each move affects the coefficients of the three sets of lines X-driven, Y-driven, and Z-driven.
We first present the strategy for the 'Step Forward' in the X direction: As in the 2D case we need to recalculate zero-intercept offsets for each slope to recalculate the line fragments array as we did in 3D SHAS. The update of the coefficients is done according to the and principle and the corresponding fragment-array columns, where each coefficient is updated for only the first or last or both slices instead for all slices as in SHAS with up to 3 or fewer operations
The Strategy for the 3D case is based on the same principles for the 2D scenario with the following adjustments; The sliding window can move 'Step Forward' (Plus) and 'Step Backward' (Minus) in three different directions according to the axes X, Y, and Z. Each move affects the coefficients of the three sets of lines X-driven, Y-driven, and Z-driven.
We first present the strategy for the 'Step Forward' in the X direction: As in the 2D case we need to recalculate zero-intercept offsets for each slope to recalculate the line fragments array as we did in 3D SHAS. The update of the coefficients is done according to the 〖𝑠𝑙𝑖𝑐𝑒〗^𝑖𝑛 and 〖𝑠𝑙𝑖𝑐𝑒〗^𝑜𝑢𝑡 principle and the corresponding fragment-array columns, where each coefficient is updated for only the first or last or both slices instead for all slices as in SHAS with up to 3 or fewer operations

## Slide 24
3D update
Dynamic SHAS

## Slide 25
3D– X-Driven update
Dynamic SHAS

## Slide 26
3D– Y-Driven update
Dynamic SHAS
Notes: The Y-driven dynamic updates are different from the X-driven updates as described for the 2D, where the additional 'fragment z' row determines a shift. As for the 2D case, some coefficients may require up to n operations, compensated by a large set of coefficients that require only re-indexing.

## Slide 27
3D– Y-Driven update
Dynamic SHAS

## Slide 28
3D– Z-Driven update
Dynamic SHAS
Notes: The Z-driven dynamic update is similar to the strategy as for the Y-driven and is illustrated. As for the 2D case, some coefficients may require up to n operations, compensated by a large set of coefficients that require only re-indexing.
The procedure for 'Step Backward' is the same as 'Step Forward' after reversing the order of and . The procedures for moving in the Y and Z direction cases are almost like in the X direction case where, for the Y direction, the Y-driven lines are updated with X-driven procedure, the Z-driven lines are updated with the Y-driven procedure, and the X-driven lines are updates with the Z-driven procedure. For the Z direction, in a similar way, the Z-driven lines are updated with the X-driven procedure, the X-driven lines are updated with the Y-driven procedure, and the Y-driven lines are updated with the Z-driven line procedure.
The Z-driven dynamic update is similar to the strategy as for the Y-driven and is illustrated. As for the 2D case, some coefficients may require up to n operations, compensated by a large set of coefficients that require only re-indexing.
The procedure for 'Step Backward' is the same as 'Step Forward' after reversing the order of 〖𝑠𝑙𝑖𝑐𝑒〗^𝑖𝑛 and 〖𝑠𝑙𝑖𝑐𝑒〗^𝑜𝑢𝑡. The procedures for moving in the Y and Z direction cases are almost like in the X direction case where, for the Y direction, the Y-driven lines are updated with X-driven procedure, the Z-driven lines are updated with the Y-driven procedure, and the X-driven lines are updates with the Z-driven procedure. For the Z direction, in a similar way, the Z-driven lines are updated with the X-driven procedure, the X-driven lines are updated with the Y-driven procedure, and the Y-driven lines are updated with the Z-driven line procedure.

## Slide 29
3D– Z-Driven update
Dynamic SHAS

## Slide 30
Running Time
Dynamic SHAS
The running time for one step in all directions
16-pixels window 2.5msec -> 400 fps
8-pixels window 250µsec -> 4000 fps
Notes: The algorithm can process images at the frame rate of the camera
The notion of real-time display is not really tied to a specific frame rate - it could be defined as the minimum frame rate at which movement is perceived as being continuous. So for slow moving objects in a visual frame (e.g. ships in a harbour, or stars in the night sky) a relatively slow frame rate might suffice, whereas for rapid movement (e.g. a racing car simulator) a much higher frame rate would be needed.
Intel® Core™ i7-6700K CPU @ 4.00GHz
(Without any parallization )

## Slide 31
Target Tracking System
Dim Target tracking application
Notes: Surveillance systems rely on remote sensors that sense energy emitted from or reflected by an object (or several objects) of interest and other sources of energy like clutter. For civilian and military applications with far imagery distance like anti-missile systems, early-warning systems, and infrared search and track systems, the target of interest often appears as a dim point embedded in a heavy cluttered background. The dim point target is typically characterized by its temporal dynamics rather than its shape (spatial) characteristics

## Slide 32
Dim Target Tracking challenges
Dim Target tracking application
s
Clutter and noise
Maneuverable target
Uncertain Data association
Real-time
Notes: Clutter and noise – From background objects like clouds, sunlight spots, and sensor noise that can cause false tracking and tracks detection misses. This issue can be handled by a background suppression (whitening( process as a part of the preprocessing stage or as an integral part of the tracking algorithm, with a goal, to suppress the clutter/ background without affecting the target signature. Article [24] presents an overview of current approaches as well as convolutional neural network-based approach for enhancement of infrared images containing a dim target.
Maneuverable target - Tracking Maneuvering targets is complicated due to the fact that acceleration is hard to model, as it can be induced by a variety of sources like atmospheric disturbances, which can cause unpredicted temporal acceleration. Sophisticated models are needed to model target motions [25, 26], and sensor measurements (like motion [27] or pixeled [28]), causing the estimation to be a nonlinear and non-Gaussian problem.
Uncertain Data association – In the broader subject of motion-based Multitarget Tracking (MTT), in addition to the target state estimation as for Single Target Tracking (STT), data association is a significant issue, since in the case of multitarget the association between measurements and tracks are uncertain. The tracking algorithm addresses this issue explicitly or implicitly by advance and sophisticated modeling [6].
Real-time – Often, it is required to finish processing a frame (or batch of frames) before the next frame arrives. Furthermore, the unpredictable and varying maneuvers of the dim target dictate a high frame rate for practical tracking purposes.

## Slide 33
Tracking Algorithms
Dim Target tracking application
Detect Before Track (DBT)
  Threshold measurement model
  High SNR scenarios
Track Before Detect (TBD)
  whole raw sensor
  Using a multi-frame to accumulate target information
  Low SNR scenarios
  Complex computation and delay
Notes:       Detect Before Track (DBT)
The general scheme in the DBT category involves detections from the sensor measurements, typically using the threshold measurement model [28], and then the thresholded measurements are fed into the tracking algorithm. The measurement-track association typically handled before the state estimation. In general, DBT methods attain good performance when tracking objects in the scenarios of high SNR. However, in low SNR, the tracking tends to fail as a large number of outliers are detected, or the target might be completely missed. A detailed description of the DBT approach can be found in [6]. The most common approaches for data association include multiple hypothesis tracking (MHT), joint probabilistic data association (JPDA), and random finite sets (RFS), and the most common approaches for estimation of target state filtering include Kalman filter and particle filter described in [30].
      Track Before Detect (TBD)
This category is also known as joint detection and tracking. The general scheme involves using the whole raw sensor data as input for tracking where relatively multiple trajectories are estimated, but no commitment is initially made for any specific trajectory. Target detection is declared after a continual tracking for the trajectory whose posterior probability is the highest. This schema improves tracking performance by using a multi-frame to accumulate target information. As no intermediate detection takes place in TBD, no explicit data association is needed. The advantage of improved performance for low SNR scenarios comes with complex computation and delay in the target tracking. The TBD methods are typically classified into Bayesian (‎2.4.3.2.1) and non-Bayesian (‎2.4.3.2.2) approaches.

## Slide 34
Track Before Detect (TBD) - Tracking Algorithms
Dim Target tracking application
  Bayesian approaches
    Handle complicated target motion using recursive Bayesian filtering approach.
    Substantial implementation cost (Particle filter)
  Non-Bayesian approaches
    Accumulate energy based on the velocity feature & use optimization algorithm.
    Efficient algorithms with real-time performance (Hough, Viterbi)
Notes:         Bayesian approaches
In Bayesian TBD approaches, the target state and measurements are described by probability density function (PDF) build from the raw sensor measurements, motions modeling, and target birth/death modeling, then recursive Bayesian filtering is applied to obtain the target state estimation. The two leading families of methods used for recursive Bayesian TBD implementations are particle filtering, and ﬁnite set statistics (FISST) based filtering described in This approach shows good results handling complicated target motion, but in general, the recursive Bayesian filter is computationally intractable and needs numerical approximation resulting in substantial implementation cost.
        Non-Bayesian approaches
In non-Bayesian approaches, at each time, the target energy in the last N frames is accumulated based on the velocity feature, and an optimization algorithm is used to ﬁnd the target track. Generally, a batch processing techniques are used where trajectories are estimated in a 3D image (a stack of 2D frames taken in uniform time intervals) with no commitment that they represent a target and only trajectories with a computed posterior probability above a certain threshold declared as targets. The non-Bayesian approaches include algorithms based on methods like multistage hypothesis testing (MHT) , 3D matched filter projective transforms as Hough and Radon [9] and dynamic programming (DP) based on the Viterbi algorithm .
Although the non-bayesian approaches are less commonly used for MTT applications, there are scenarios where the target trajectory constitute a straight line or as a chain of straight line segments (piecewise constant velocity target) assuming that the curved trajectory sampled can be well approximated by breaking it into intervals in which for each interval velocity is treated as a constant. For this kind of particular scenarios, there are efficient versions of non-bayesian algorithms with real-time performance, for example, the Viterbi algorithm used as part of unmanned aerial vehicle (UAV) collision avoidance system and the Hough transform used as part of detecting low radar cross-section targets application.

## Slide 35
Target Model/Measurement Model
Dim Target tracking application
scenarios where the target trajectory constitute a straight line or as a chain of straight line segments (piecewise constant velocity target) assuming that the curved trajectory sampled can be well approximated by breaking it into intervals in which for each interval velocity is treated as a constant
, pixel
pixel
sub-pixel target
entire support inside a single pixel.
Notes: The target state at time consists of the target position and its first derivative.
The next linear stochastic process models the state progression
Where denotes a model noise and A denotes the transition matrix
With the next constrains:
Our interest is in the detection of a sub-pixel target, which is significantly smaller than pixel size, where there is no need to take into account the target point spread function, which is assumed to have its entire support inside a single pixel. In all our experiments, we normalize the target intensity to one, and the noise level and resulting SNR are determined accordingly to this normalized value.
-----
we normalize the target intensity to one, and the noise level and resulting SNR are determined accordingly to this normalized value.
The target state at time 𝑖,𝑣_𝑖 consists of the target position and its first derivative.
The next linear stochastic process models the state progression
Where 𝑛_𝑖 denotes a model noise and A denotes the transition matrix
With the next constrains:
Our interest is in the detection of a sub-pixel target, which is significantly smaller than pixel size, where there is no need to take into account the target point spread function, which is assumed to have its entire support inside a single pixel. In all our experiments, we normalize the target intensity to one, and the noise level and resulting SNR are determined accordingly to this normalized value.
-----
we normalize the target intensity to one, and the noise level and resulting SNR are determined accordingly to this normalized value.

## Slide 36
Dynamic SHAS Based Tracking
Dim Target tracking application
Notes: The windows continue tracking till they got lost event
Handling the predictions according to the windows maximum coeff. values is a topic outside the scope of the thesis .
As we concentrate on one target that start and never die we offer simple paradigm of setting the prediction according to the window with the maximum coeff. Value.

## Slide 37
Experiments Methodology
SHAS
  ‘Detection’ criteria
  ‘Tracking’ criteria
Dynamic SHAS
  Straight trajectory
  Curved trajectory
  Straight with model noise trajectory
Viterbi
Clouds scene

## Slide 38
The 3D X-Ray Transform
SHAS vs other X-ray approaches
As
Notes: Scientific area that deals with…..

## Slide 39: DSHAS: Why Sliding Window ?
Constraints on memory and speed (moderate cube 643 => 1.5 Gb of coefficients)
Shift-invariant
Dynamic Region of Interest
Fast

## Slide 40
Background
Bcvbcbv
Bcvbcv
Bcvbcb
Bcvcbvc
cbvbcb